|  | D.C MOTOR DATA SHEET | HICO S.O. DM10226 |
| --- | --- | --- |
| SHEET OF | CUSTOMER : |  | ITEM NO. : |
| FOR PROPOSAL | JOB NO. : |  |  |
| DESCRIPTION : |  | SITE : |  | QUANTITY : 1 SET |
| GENERAL DATA | PERFORMANCE DATA |
| FRAME NO. | LAP112-2M | OUTPUT | 2.2 KW ( HP) |
| TYPE | SPEED | 1750 R.P.M |
| ENCLOSURE | DP(IP23S) | ARMATURE |
|  | ARM. VOLTAGE | 440 | V |
| COOLING METHOD* | IC 06 | FULL LOAD CURRENT | 6.0 | A |
|  | FIELD |
| POWER SUPPLY | NEMA C | POLES | 2 |
|  | WINDING TYPE | SEP. – SHUNT |
| INSULATION CLASS | F |  |  |
| TEMP. RISE AT FULL LOAD | FIELD VOLTAGE | 180 | V |
|  | RES. METHOD | 105 (C | FIELD CURRENT | 1.8 | A |
|  | THERMO. METHOD | 85 (C | FIELD RES.(AT25(C) | 74.19 | Ω |
| LOCATION | INDOOR | EFFICIENCY |
| ALTITUDE | LESS THAN 1000M |  | AT 1/2 LOAD | - | % |
| HUMIDITY | LESS THAN 80% |  | AT 3/4 LOAD | - | % |
| AMBIENT TEMP.(MAX.) | 40 (C |  | AT FULL LOAD | 72 | % |
| RATING | CONTINUOUS |  |  |  |
| ROTATION | C.W | FULL LOAD TORQUE | 1.22 | Kg.m |
| MOUNTING | B3 (HORIZONTAL) | MOTOR GD2 | 0.12 | Kg.m2 |
| BEARING TYPE | ANTI FRICTION | CARBON BRUSH |
| FRONT / REAR BRG. NO. | 6305 / 6307 | BRUSH MATERIAL | EG283 |
| BRG. LUBRICATION | GREASE | BRUSH SIZE | 12.5x16x28 |
| SERVICE FACTOR | 1.00 | MOTOR APPROX. WEIGHT | 110 | Kg |
| DRIVE | DIRECT COUPLED | PAINTING | 8B 4.5/3.25 | (URETOP) |
| SHAFT | SUBMITTAL DRAWINGS |
|  | EXTENSION | SINGLE | OUTLINE DIMENSION | 1DE10301H01 |
|  | VERTICAL |  | CONDUIT BOX & COVER | 1DO 00425 |
|  | EXTERNAL THRUST |  | TERMINAL DIAGRAM | 1DO 00426 |
| MOTOR MOUNTED BLOWER | . |  |
|  | OUTPUT | 0.5HPX2P |  |  |
|  | VOLTAGE | 440 | V | <NOTE> EXCEPT FOR STATEMENTS SPECFIED ON THIS |
|  | PHASE/FREQUNCY | 3 PHASE 60Hz | SHEET,ANYTHING ELSE SHALL BE IN ACCORDANCE |
| MOTOR MOUNTED TACHO-GENERATOR | WITH HYOSUNG STANDARS. |
|  | TYPE | 104-8011-1 |  |
|  | OUTPUT | 30V/1000RPM |  |
|  | MAKER | SANYO | <REMARKS> |
| TERMINAL BOX |  |
| MAIN | HYOSUNG STD. |  |
| AUX. |  |  |
| APPLICATION STANDARDS |  |
| IEC 34 |  |
| <NOTE> THE DATA OF THE DARK LINE MUST BE CHECKED FOR |  |
| SPARE MOTOR. IF THE CONTROL PANEL DOES NOT |  |
| SATIFY THE REQUIRMENTS, IT MUST BE ADJUSTED. |  |
|  | REV. NO | DATE | PREPD BY | CHKD BY | REV. NO |
| *IC06 : MOTOR MOUNTED FAN AND FREE CIRCULATION IC17 : PIPE VENTILATED INLET DUCT AND FREE CIRCULATION IC37 : PIPE VENTILATED INLET AND OUTLET DUCTS IC0041 : TOTALLY ENCLOSED IC0641 : TOTALLY ENCLOSED,FAN COOLED ** ROTATION : SHAFT EXTENTION VIEW | 0 | 2011.12.01 | Y.H.JANG | K.S.LEE | K.S.LEE |